Ham Supply Yaesu Illuminator G-450/650 Installation Instructions

Presently the Yaesu Illuminator G-450/650 3 LED Board installs in G-450 and G-650 series rotor controllers. As we confirm operational success in “unlisted” controllers, we will update these instructions and our Website accordingly.

Unplug the rotator control box from the mains power supply.  Unplug the rotator antenna cabling plug on the rear of unit.  Utilize a clear and open workbench, table, etc. for installation of your Yaesu Illuminator G-450/650 Board.

Remove 8 Phillips screws on the rotator control box.  4 rubber feet, 2 between the rubber feet bottom and 2 from the sides (one each side). Set those 8 screws aside as you will reuse them in reassembly.

Gently pull apart the control box with two hands.  The “face” including the compass meter in one hand, the outer rotator control “shell” with the other.  There is no need to unplug any connectors or disconnect any block connectors to internal boards at this time.  Once separated, remove the two countersunk Phillips head screws on the top of the plastic face and 3 more connecting the bottom face.

On the inner face “half”, locate and remove 1 upper (center) screw that is used for mounting the existing compass style meter to the plastic front bezel. See picture #1. We will use this single screw to mount the Yaesu Illuminator G-450/650 3 LED Board. You may discard the single Phillips panhead screw as it will be replaced with our longer Yaesu Illuminator Phillips panhead screw included with your new board.

With the 3 Clear LED’s facing the compass meter (under the compass meter metal mount) and with the components on the Yaesu Illuminator Board facing UP, mount the new board. Use the screw and nylon spacer provided. Proceed to tighten the Phillips panhead screw. Do not over tighten. Take a few moments to inspect your work and answer “yes” to these questions. “Are the 3 LED’s on the Yaesu Illuminator facing the meter compass? Is the new board mounted parallel to the rear meter face? Are the components (diode, resistor, etc.) facing UP and away from the back of the meter face? Is the nylon spacer between the rear of the meter face and the board? Is the mounting screw snug?”

If you answered yes to all questions, proceed to locate the 2 wires going to the upper left of the compass meter (viewing from the front of compass meter). Picture #2. Viewing from the rear of the face half, these 2 wires are in the upper right top corner of the control box. These 2 wires are the power wires to the original hi-intensity, non-serviceable bulb you are replacing. The bulb is not visible, but these 2 feed wires are. There is no other wiring near these 2 wires. Snip those two wires as close as possible to the bulb. These are the two wires providing 12V that connect to the black and red Yaesu Illuminator Board wires.

Connect the RED Positive wire on the Yaesu Illuminator to the controller 12V Positive, the BLACK Negative on the Yaesu Illuminator wire to the controller Negative. At this point with the front halves separate and all wiring clear of obstructions, check that your Yaesu Illuminator LED board is working and hooked up correctly. Plug unit in to the mains, depress the Power button and note the 3 LED’s light. IF your connections are reversed, the LED’s will not light as they are diode protected. Check the 3 LED’s positioning and adjust as necessary with a plastic insulated screwdriver. Unplug from mains and continue with permanent wire splices. Some technicians utilize solder and shrink tube for their connections; others strip and crimp. We leave the 12V connections to whatever type of connection you are personally comfortable with. After splicing and sealing, check to make sure the wires do not interfere with any components. Picture #3.

Slide the 2 halves together and reinstall the 5 screws - 2 countersunk on the top plastic face and 3 on the bottom plastic face. Install the shell cover and install the 2 sides, 2 bottom, and 4 rubber feet screws.  You have completed the installation of your Yaesu Illuminator G-450/650 3 LED Board!

High resolution pictures are available at:  http://www.hamsupply.com/support/ under “Yaesu Illuminator G-450/650”.